LED8N Customer Display

User’s Manual

INTERFACE SPECIFICATIONS

1、 Communication

The interface specification are based on EIA USB 2.0 baud rate 2400 bps, 8 data bits, no parity, 1 stop bits.

2、Power connector

Connector type: USB power (DC5V/500MA)

3、EPSON ESC/POS commands instruction set list

STX  B  n

Name：select baud rate

ACSII：STX  B  n

Decimal：002  066  n

Hex：02H  42H  n

Description：When the power is turned on, the default value of n is 0(set to 2400)

| ASCII n | Decimal n | Hex n | Baud rate |
| --- | --- | --- | --- |
| 0 | 48 | 30H | 9600 |
| 1 | 49 | 31H | 4800 |
| 2 | 50 | 32H | 2400 |
| 3 | 51 | 33H | 1200 |
| 4 | 52 | 34H | 600 |
| 5 | 53 | 35H | 300 |

- STX  L  d1  d2  d3  d4

Name：Control the display status lights

ACSII：STX  L  d1  d2  d3  d4     d=0、1

Decimal：[002][076]d1 d2 d3 d4        d=048、049

Hex：[02H][4CH]d1 d2 d3 d4          d=30H、31H

d1=0，Price  Dark；d1=1，Price  Bright

d2=0，Total  Dark；d1=1，Total  Bright

d3=0，Collect  Dark；d1=1，Collect  Bright

d4=0，Change  Dark；d1=1，Change  Bright

- CR

Name：move the cursor to left-most position on the current line

ACSII：CR

Decimal：13

Hex：0D

- ESC  @

Name：initialize display

ACSII：ESC  @

Decimal：27  64

Hex：1B  40

Description：The software settings are reset to their power-on values. After initializing the display, the display screen is cleared and the cursor moves to the home position.

- CLR

Name：clear display screen

ACSII：CLR

Decimal：12

Hex：0C

Description：Clear all the displayed characters.After this command is executed, the cursor moves to the home position.

- CAN

Name：clear cursor line, and clear string mode

ACSII：CAN

Decimal：24

Hex：18

Description：Clears the line containing the cursor.After this command is executed, the cursor moves to the left-end position on the current line.

- ESC  Q  A  d1d2d3…dn  CR

Name: Display data command

ASCII：ESC  Q  A  d1d2d3…dn  CR

Decimal：[027][081][065]d1d2d3…dn[013]     48<=dn<=57   dn=45  dn=46

Hex：[1BH][51H][41H]d1d2d3…dn[0DH]     30H<=dn<=39H   dn=2DH   dn=2EH

Description：

- When the command is executed, will be sent to cover the mode you want to display data.

- d1 ... dn display no decimal point  1 <= n <= 8。

- d1…dn display the decimal point 1<=n<=15（8-bit digital +Seven decimal places）。

- Display the contents of the available CLR or CAN commands to clear。

- ESC  s  n设置 “Price”、“Total”、“Collect”、“Change”

Name: display character state command

ASCII：ESC  s  n                    0<=n<=4

Decimal：[027][115] n                  48<=n<=52

Hex：[1BH][73H] n                30H<=n<=34H

Description：

      - n=0，Character is all dark。

      - n=1，“Price” Bright characters, the other three all-dark。

      - n=2，“Total” Bright characters, the other three all-dark。

      - n=3，“Collect” Bright characters, the other three all-dark。

      - n=4，“Change” Bright characters, the other three all-dark。